Cowichan Koksilah Recovery Actions, reviewed July 2007

The CSRT group went through an update cycle and had the opportunity to review a number of projects and programs on the original Cowichan Recovery Plan developed in 2005 by LGL for Cowichan Tribes and provided to this group as a guiding document.  The key projects identified for the upcoming period include the twelve summarized below.  The original tabular data has been updated with information provided and is also attached for the groups review and additional comments.

1) Implementation of the CBWMP - this is consistent with the highest priority of the Cowichan Recovery Plan (LGL Ltd. 2005), and should focus on the steps necessary to raise storage behind the Catalyst weir by 30cm, and install low-head pumps for extreme drought protection.  We have budgetted $40K in our 2007 Georgia Basin/Vancouver Island Living Rivers Program for WMP implementation activities.  These funds could be used to help map Cowichan Lake shoreline properties (LIDAR technology), relative to required mitigation/compensation under the Water Act.  We await the planned vote by the CVRD's Committee of the Whole on moving forward with a WMP implementation strategy ASAP.  UPDATE CVRD’s Committee of the Whole did not ratify a number of key initiatives identified in the report including, raising of wer, application for water license, adjustment of rule curve or implementation of governance model.  The CSRT will have to discuss next course of action relative to this implementation item.

(2)  Sediment management downstream of Cowichan Lake - this is consistent with the second highest priority in the Cowichan Recovery Plan.  The focus of this work in the next 1-2 years will remain Stoltz Bluff until we are satisfied we have remedial measures/designs well in-hand.  Worked planned for September 2007 should take us a long way towards this goal.  Annual maintenance of new sediment deposits on the constructed terrace will be an on-going issue, but may become less so as new "ring berms" at the base of existing gullies start to retain material and build shallower angles of repose back into the existing steep slope.  Further geotechnical studies may lead to upslope treatment strategies, including surface/groundwater controls at the top of the bluff.  Bio-engineering of exposed soils on the bluff, as well as on the terrace, will be considered pending success of this year's initial soil wrap and live-staking experiments.

(3)  A second phase of sediment management may be launched at sites upstream of Skutz Falls (3 Firs; Block 51), pending results of this year's sediment source surveys and preliminary plans for future remediation.  BCCF is working with LGL Ltd. (Marc Gaboury) and possibly TROW Engineering Ltd. (Jim O'Brien, P.Eng.) on this initiative.  Proposed remediation works could be funded by Georgia Basin/VI Living Rivers, PSC (Southern Fund), HCTF and others, as required.

(4)  On-going TSS/turbidity monitoring has been led by DFO (Margaret Wright, Water Quality Biologist) in an attempt to provide early results from the 2006 work at Stoltz Bluff.  This should be continued in the winter of 2007/08.  More detailed biophysical monitoring of the results of sediment management may be funded by the Pacific Salmon Commission in 2008/09.

(5)  Sediment management in upstream reaches of the river should be directly linked to flood control and gravel removal activities in the lower floodplain, within Duncan city limits and Cowichan Tribes Reserve #1.  Gravel removal at the Catalyst pumphouse should also be brought under this "umbrella."

(6)  Estuary protection, rehabilitation and land puchase.  Work collaboratively with the Cowichan Community Land Trust (Ann Archibald), Cowichan Tribes, DFO, TNT, TLC, DUC and other partners on an ambitious plan for estuary restoration and preservation.  Georgia Basin/VI Living Rivers and PSC to assist with funding requirements.   Support review of CEEMP planning process.

(7)  The Trestle Side-Channel re-design project is proceeding through the BC Parks' approval process, led by BCCF, nhc Ltd. and DFO.  The improvement of this channel is considered a high priority for chinook and coho production upstream of Skutz Falls, assuming sustained flows can be provided through a new intake structure.  Funds to implement the recommended new intake design could be forthcoming from Georgia Basin/VI Living Rivers and PSC in 2008 (this will require a PSC concept letter be prepared by the August 26/07 deadline).

(8)  Other side-channel improvement projects identified by Gaboury (2004) and others should be considered for funding on a priority basis, particularly in relation to how well they meet the CSRT and DFO's objectives for chinook and coho rebuilding.  These could include, but not be limited to Lamb's side-channel, Channel 83A, Bonsall Slough and Major Jimmy's side-channel.  Re-design and construction would take place over the next 3 years based on funding availability.   See tabular data below

(9)  Pilot-scale spawning gravel placements in the outlet of Cowichan Lake.  Historic spawning areas within the first 1.5 km of the Catalyst Paper weir have become depleted of quality spawning gravel based on snorkel surveys conducted by MoE and BCCF in the late spring of 2006.  Most of these sites overlap with a few riffle crests in a reach dominated by deep pool and glide habitats.  The objective would be to target 1-2 riffles crests for experimental gravel placements using low-tech equipment (barge and bobcat or excavator with extended arm/reach off bank).  All gravel would be screened and double-washed to minimize sediment release in a developed area with high recreational use.  The sites would be selected this year and a proposal prepared for funding consideration.  Georgia Basin/VI Living Rivers would likely be the primary funding source for implementation in the summer of 2008.  Monitoring of fish use would start in the fall of 2008.

(10)  Riparian management/silvicultural treatments should be considered on all public lands downstream of Cowichan Lake, where necessary.  This would be done under direction of a contract RPF, or with assistance from the Ministry of Forests.  Priority attention should be given to sites within the BC Parks' linear protected area along the river where bank erosion is now evident.  This could ultimately be combined with action item #3 above, and the river upstream of Skutz Falls should be the highest priority.

(11)  Maintenance of Skutz Falls fishway.  This needs to be assessed annually to ensure the fishway is unobstructed by debris and bedload to ensure the most efficient passage of spawning salmon and steelhead.

(12)  Survey of restoration opportunities in tributaries to Cowichan Lake, including but limited to Robertson River, Shaw Creek, Nixon Creek, Sutton Creek, Meade Creek and Cottonwoood Creek.

- Survey of restoration opportunities in the Koksilah River, building on work to be done by LGL Ltd. (Marc Gaboury) and Cowichan Tribes in 2007.

Stock Status and Recovery Actions

Appendix D1 Table of recovery actions to address critical uncertainties in stock status and hatchery effectiveness with preliminary project designs and cost estimates (donated labour and materials are costed for the purposes of this recovery plan). Note that some of these SS projects will also contribute to monitoring the recovery plan.

| Project Code | Uncertainty Issue | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded? |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SS-1 Currently funded | Escapement | Cowichan River | Cowichan mainstem | Fall Chinook, coho, chum | Adult | 2005 | 20 | Annual | $100,000 | $2,000,000 | 1. Installation, maintenance and operation of counting weir on Cowichan ($85,000 per year) 2. Achieve precision of ±15% (mark recapture if necessary) 3. Annual reporting of results ($15,000) 4. Construction and maintenance of weir is amortized over 20 years | Annually (DFO-AFS) Currently funded |
| SS-2 Currently funded | Escapement | All | Somenos, Kelvin, Robertson, Shaw, Patricia | Coho | Adult | 2005 | 20 | Annual | $35,000 | $700,000 | 1. Conduct visual surveys of 5 tributaries throughout CRPA using walks and/or swims (approximately 5 surveys per system per year) ($6,000 per system per year) 2. Achieve precision of ±30% using AUC analysis 3. Expand estimates from tributaries to entire CRPA using habitat expansion as per Bocking and Peacock (2005). 4. Annual reporting of results ($5,000) | Some Years (DFO) Currently funded |
| SS-3 Currently funded | Escapement | Cowichan River | Cowichan mainstem | Chum | Adult | 2005 | 20 | Annual | $30,000 | $600,000 | 1. Conduct visual surveys of lower Cowichan using helicopter as well as walks of key areas (approximately 5 surveys per year) ($6,000 per system per year) 2. Achieve precision of ±30% using AUC analysis 3. Annual reporting of results ($5,000). | Annually (DFOAFS) Currently funded |
| SS-4 | Escapement | Cowichan River, Cowichan Lake Tributaries | Robertson? Upper Cowichan mainstem? | Spring Chinook | Adult | 2006 | 20 | Annual | $7,500 | $150,000 | 1. Identify spawning areas for spring Chinook and conduct visual surveys using swims/walks (approximately 3 surveys per year ($5,000 per year) 2. Achieve precision of ±30% using AUC analysis 3. Annual reporting of results ($2,500). | No |
| SS-5 No longer funded | Escapement | Cowichan River, Koksilah River | Cowichan mainstem, Koksilah mainstem | Steelhead | Adult | 2006 | 20 | Annual | $15,000 | $300,000 | 1. Establish index sites and conduct visual surveys on Cowichan and Koksilah using swims (approximately 5 surveys per year) ($10,000 per year) 2. Achieve precision of ±30% using AUC analysis (for index sites) or expanded peak count 3. Annual reporting of results ($5,000). | Some years (MWLAP) No longer funded |
| SS-6 | Escapement | Koksilah River | Koksilah mainstem | Fall Chinook, coho, chum | Adult | 2005 | 20 | Annual | $15,000 | $300,000 | 1. Conduct visual surveys on Koksilah using swims (approximately 5 surveys per year) ($10,000 per year) 2. Achieve precision of ±30% using AUC analysis or expanded peak count 3. Annual reporting of results ($5,000). | No |
| SS-7 | Juvenile production | Cowichan River | Cowichan mainstream | Chinook, coho, steelhead | Fry, Parr, Smolts | 2006 | 20 | Annual | $100,000 | $2,000,000 | 1. Conduct downstream trapping study using mark-recapture design and RSTs (March – end of June) (4 months at $21,250 per mo) 2. Generate mark-recapture estimates (±20%) and evaluate hatchery contributions to freshwater production | Annually during 1990s Started |

| Project Code | Uncertainty Issue | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded? |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  | 3. Annual reporting of results ($15,000). | again in |
|  |  |  |  |  |  |  |  |  |  |  |  | 2005 |
|  |  |  |  |  |  |  |  |  |  |  |  | (DFO) |
| SS-8 | Juvenile production | Koksilah River | Koksilah mainstem | Chinook, coho, steelhead | Fry, Parr, Smolts | 2006 | 20 | Every 4 years | $50,000 | $200,000 | 1. Conduct downstream trapping study using mark-recapture design and RSTs (March – end of June) (4 months at $10,000 per mo) (Note – add on costs to Project SS-7) 2. Generate mark-recapture estimates (±20%) and evaluate hatchery contributions to freshwater production 3. Annual reporting of results ($10,000). | No |
| SS-9 | Juvenile production, marine survival | Cowichan Lake, Cowichan River, Koksilah | Kelvin Creek, Somenos, Robertson (or Shaw, or lake aggregate) | Coho | Fry, Parr | 2006 | 3 | Annual | $50,000 | $150,000 | 1. Coded-wire tag approximately 30,000 juvenile coho emigrating from 1 of 3 zones in CRPA in each of 3 years 2. Compare marine survival rates from Cowichan with Black Creek and Vancouver Island hatchery coho 3. Annual reporting of results ($10,000). 4. If results indicate that Cowichan marine survivals are very different, then continue with monitoring | No |
| SS-9a | Fry Salvage | Tributary – mainstream to lake |  | Coho |  |  |  |  |  |  | Tom Rutherford has plan with details.. |  |
| SS-10 | Catch | Cowichan River, Koksilah River Cowichan Bay | Cowichan River, Koksilah River Cowichan Bay | Chinook, Chum, Coho | Adult | 2005 | 20 | Annual | $30,000 | $600,000 | 1. Conduct creel survey of all terminal fisheries (sport and Cowichan tribes in CRPA (including Bay and River) 2. Annual reporting of results ($10,000). | Partial (DFOAFS) |
| SS-11 | Hatchery effectiveness | Cowichan River | Cowichan mainstem | Fall Chinook | Fry | 2006 | 5 | Annual | $50,000 | $250,000 | 1. Coded-wire tag 250,000 fall Chinook fry from hatchery for next 5 years to evaluate hatchery effectiveness 2. Monitor returns in Project SS-1 and through catch monitoring in fisheries 3. Annual reporting of results ($10,000). | Partial (DFO) Currently funded ~200,000 annually, last year $275,000 |
| SS-12 | Hatchery effectiveness | Cowichan River | Cowichan mainstem | Spring Chinook | Fry | 2006 | 10 | Annual | $10,000 | $100,000 | 1. Coded-wire tag all spring Chinook fry from hatchery for next 10 years to evaluate hatchery effectiveness 2. Monitor returns in Project SS-1 and through catch monitoring in fisheries 3. Annual reporting of results | No |
| SS-13 | Hatchery effectiveness | Cowichan River | Cowichan mainstem | Steelhead | Parr | 2006 | 20 | Annual | $5,000 | $100,000 | 1. Coded-wire tag all steelhead parr from hatchery to evaluate hatchery effectiveness and enable marked fishery 2. Annual reporting of results 50,000 adipose clip | Annual (MWLAP) $? NO assessment funding |
|  |  |  |  |  |  |  |  | Totals | $497,500 | $7,450,000 |  |  |

Population Gains

Appendix D2 Table of recovery actions to directly affect population gains with preliminary project designs and cost estimates (donated labour and materials are costed for the purposes of this recovery plan).

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded? |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PG-1 | Harvest Rates | Marine / Cowichan Recovery Planning Area | Marine / Cowichan Recovery Planning Area | Fall Chinook | Adult | 2005 | 20 | Annual | $10,000 | $200,000 | 1. Develop annual harvest management plans for fall Chinook based on marine survivals, freshwater survivals, escapement objectives 2. Target maximum harvest rate of 25% during recovery Current estimates are 65-70% 3. Prepare annual fishing plan | Annual (DFO-AFS, CT, other sectors) |
|  |  |  |  |  |  |  |  |  |  |  | Some concern was expressed at the last meeting that a discussion regarding sustainable harvest rates should take place at the Harvest Roundtable not in our documents and workplans... |  |
| PG-2 | Hatchery | Cowichan River | Cowichan River | Fall Chinook | Adult | 2005 | 20 | Annual | $500,000 | $10,000,000 | 1. Continue with hatchery supplementation of fall Chinook 2. Annual reporting of results ($10,000) | Annual (DFO) |
| PG-3 | Harvest Rates | Cowichan River | Cowichan mainstem | Spring Chinook | Adult | 2005 | 20 | Annual | $5,000 | $100,000 | 1. Develop annual harvest management plans for spring Chinook based on marine survivals, freshwater survivals, escapement objectives 2. Prepare annual fishing plan | No |
| PG-4 | Hatchery | Cowichan River | Cowichan River | Spring Chinook | Adult | 2005 | 20 | Annual | $50,000 | $1,000,000 | 1. Hatchery supplementation of spring Chinook 2. Annual reporting of results ($10,000) | No |
| PG-5 | Hatchery | Cowichan River | Cowichan River | Coho | Fry | 2005 | 20 | Annual | $25,000 | $500,000 | 1. Continue fry salvage program | Some |
| PG-5 | Harvest Rates | Marine / Cowichan Recovery Planning Area | Marine / Cowichan Recovery Planning Area | Chum | Adult | 2005 | 20 | Annual | $15,000 | $300,000 | 1. Develop annual harvest management plans for chum based on marine survivals, freshwater survivals, escapement objectives 2. Target maximum harvest rate of 20% during recovery 3. Cost includes DNA sampling to enable separation of Cowichan stock from other stocks in mixed-stock fisheries ($10,000 per year amortized over 20 years) 4. Review stock composition estimates on annual basis 5. Prepare annual fishing plan | Annual (DFO-AFS, CT, other sectors) |
| PG-6 | Harvest Rates | Cowichan River, Koksilah River | Cowichan River, Koksilah River | Steelhead | Adult | 2005 | 20 | Annual | $5,000 | $100,000 | 4. Develop annual harvest management plans for steelhead based on marine survivals, freshwater survivals, escapement objectives 5. Prepare annual fishing plan | Annual (MWLAP) |
| PG-7 | Hatchery | Cowichan Bay | Cowichan Bay | Clams |  | 2006 | 3 | Annual | $15,000 | $45,000 | 1. Experimental seeding of beaches 2. Reporting and evaluation | No |
|  |  |  |  |  |  |  |  | Totals | $625,000 | $12,245,000 |  |  |

Habitat Knowledge Actions

Appendix D3. Table of recovery actions to directly affect habitat knowledge with preliminary project designs and cost estimates. (donated labour and materials are costed for the purposes of this recovery plan).

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HK-1 | Identify Lake Rearing Habitat | Cowichan Lake | Cowichan, Bear, Mesachie lakes | Coho | Fry | 2006 | 2 | Annual | $20,000 | $40,000 | 1. Assess littoral areas of Cowichan, Bear, and Mesachie lakes to identify and characterize primary coho rearing habitat 2. Identify protection and rehabilitation opportunities | No |
| HK-2 | Watershed Assessment | Cowichan Lake Tributaries | Robertson, Sutton, Nixon, Shaw, Meade, Cottonwood | Coho, Steelhead | Fry, Adult, Parr | 2008 | 2 | Annual | $50,000 | $100,000 | 1. In cooperation with private land owners, conduct watershed and habitat assessments on three tributaries each year to determine condition of watershed, probable causes of channel disturbance and instability, critical limiting factors for coho and steelhead, and rehabilitation opportunities. 2. Prioritize potential rehabilitation works and develop rehabilitation designs for specific sites within high priority reaches where there is a high likelihood of rehabilitation success. 3. Determine preliminary costs for high priority rehabilitation designs. | No |
| HK-3 | Reduce Sediment Loads and Improve Sediment Management | Cowichan River Mainstem | Stoltz Slide, Block 51 and other significant sediment sources | Chinook | Fry, Adult, Parr | 2005 | 1 | n/a | $60,000 | $60,000 | Conduct preliminary investigations to identify / measure / map major sediment sources in the watershed below Lake Cowichan, quantify sediment loading rates, and link loading rates and sediment composition to biological effects on fish habitat and production. The latter need should be facilitated by a current DFO study of Chinook salmon egg incubation conditions and success, relative to known sediment sources, loading rates and gravel quality. 2. Assess and cost a range of geotechnical and engineering options designed to significantly reduce sediment loading of the river, for priority point sources identified above. This phase will produce detailed engineering surveys/designs for the major sediment source at Stoltz Slide as well as other problem sites that are identified in the synoptic survey above. 3. Develop a preliminary Cowichan River Sediment Management Plan that identifies sources, quantities, composition, remedial measures and a monitoring program to determine the effectiveness of remediation. This will be presented as a draft to stakeholders for review and consensus on future actions, timeframes and joint funding requirements. Stolz Slide work and remediation ongoing through 2008 with replanting and analysis of upslope failure initiation zones. Maintenance of structures and benches in lower sections ongoing. | PSC funding sediment assessments and DFO study in 2005 Ongoing |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HK-3a | Sediment budget for lower Cowichan | Cowichan Mainstem | Lower Cowichan Mainstem | Coho, Chinook, Chum | Fry, Adult Parr | 2008 | 1 |  |  |  | Development of sediment budget and Floodplain analysis relative to dyke control features and maintenance. | No, funding proposals developed and forwarded to UBCM |
| HK-4 | Improve Summer Flows and Water Temperatures | Cowichan River Mainstem | Cowichan River Mainstem | Coho, Chinook, Chum, Steelhead | Fry, Adult, Parr | 2005 | 1 | n/a | $150,000 | $150,000 | Develop a Water Management Plan for Cowichan River and consider increasing potential water storage by raising the Cowichan Lake Weir height thereby increasing summer flows in the mainstem, and re-establishing connectivity to off-channel and tributary areas. 2. Assess feasibility and benefits of a deep water lake discharge to the river to reduce high summer temperatures. Water Basin Plan recommendations and report received and amended by CVRD Board September 2008. Demand Management options accepted. Supply side options not currently supported by CVRD Board of Directors. No support provided to the amendment of rule curve variations. | Water Management Study completed |
| HK-5 | Watershed Assessment | Cowichan River Tributaries | Holt | Coho, Steelhead | Fry, Adult, Parr | 2010 | 1 | n/a | $30,000 | $30,000 | 1. In cooperation with private land owners, conduct watershed and habitat assessments to determine condition of watershed, probable causes of channel disturbance and instability, critical limiting factors for coho and steelhead, and rehabilitation opportunities. 2. Prioritize potential rehabilitation works and develop rehabilitation designs for specific sites within high priority reaches where there is a high likelihood of rehabilitation success. 3. Determine preliminary costs for high priority rehabilitation designs. | No |
| HK-6 | Watershed Assessment | Cowichan River Tributaries | Somenos | Coho | Fry, Adult, Parr | 2006 | 1 | n/a | $40,000 | $40,000 | 1. In cooperation with private land owners, conduct watershed and habitat assessments to determine condition of watershed, probable causes of channel disturbance and instability, critical limiting factors for coho and steelhead, and rehabilitation opportunities. 2. Prioritize potential rehabilitation works and develop rehabilitation designs for specific sites within high priority reaches where there is a high likelihood of rehabilitation success. 3. Determine preliminary costs for high priority rehabilitation designs. | No |
| HK-7 | Watershed Assessment | Cowichan River Tributaries | Somenos, Quamichan | Coho | Fry, Adult, Parr | 2006 | 3 | Annual | $100,000 | $300,000 | Limnological Assessments 2. Hydrological Assessments 3. Fish Assessments Quamichan Lake Stewardship group formed and actively seeking project funding. | No |
| HK-8 | Assess Culvert / Fish Passage | Cowichan River Tributaries | Skutz Creek, Holt and tributaries | Coho | Adult, Fry | 2008 | 1 | n/a | $40,000 | $40,000 | 1. Conduct culvert / fish passage assessment. 2. Develop plans of remedial measures to ensure fish passage. | No |
| HK-9 | Watershed Assessment | Koksilah River & Tributaries | Mainstem, Glenora, Kelvin, Norrie | Coho, Chinook, Chum, Steelhead | Fry, Adult, Parr | 2010 | 2 | Annual | $40,000 | $80,000 | 1. In cooperation with private land owners, conduct watershed and habitat assessments to determine condition of watershed, probable causes of channel disturbance and instability, critical limiting factors for coho and steelhead, and rehabilitation opportunities. | No |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  | 2. Prioritize potential rehabilitation works and develop rehabilitation designs for specific sites within high priority reaches where there is a high likelihood of rehabilitation |  |
|  |  |  |  |  |  |  |  |  |  |  | success. |  |
|  |  |  |  |  |  |  |  |  |  |  | 3. Determine preliminary costs for high priority rehabilitation designs. |  |
| HK-10 | Assess Culvert / Fish Passage | Koksilah River & Tributaries | Koksilah River & Tributaries | Coho | Adult, Fry | 2008 | 1 | n/a | $20,000 | $20,000 | 1. Conduct culvert / fish passage assessment. 2. Develop plans of remedial measures to ensure fish passage. | No |
| HK-11 | Hydrological Modeling and Feasibility of Setback Dyking | Cowichan Estuary | Quamichan, Hatchery, and South Side Spur dykes | Chinook, Chum, Coho, Steelhead | Fry, Adult, Parr | 2006 | 1 | n/a | $80,000 | $80,000 | 1. Conduct preliminary investigations to assess the effects of current dyking in the lower river on floodwater routing and sediment deposition / transport. Topographic survey data of the channel and floodplain, and historical flow records would be required to model effects. 2. Assess feasibility of removing specific dykes and reconstructing setback dykes. Model effects of setback dykes on floodwater routing and sediment deposition / transport. Determine the positive and negative effects of setback dyke construction on fish and fish habitat, flood risk, sediment deposition and transport, etc. Examine effects of gravel removal and determine need and potential locations for regular gravel extraction from the river. 3. If feasible and net effects are positive, determine preliminary costs for setback dyke option. This phase will produce conceptual engineering designs for the setback dykes. | No 2007 Funding proposal developed and requested from UBCM for a portion of the Hydrological modeling process. |
| HK-12 | Intertidal Mapping of Substrate, Vegetation and Fauna | Cowichan Estuary | Cowichan Estuary | Chinook, Chum, Coho, Steelhead, Shellfish | All | 2005 | 1 | n/a | $50,000 | $50,000 | 1. Complete inter-tidal mapping of substrate, vegetation and fauna. 2. Develop rehabilitation plan for estuary including protecting / re-establishing vegetation, shellfish, etc. | Cowichan Tribes funded Archipelago for Phase 1 in 2005 |
| HK-13 | Identify Densities of Bivalves on Beaches | Cowichan Bay | Cowichan Bay | Clams | n/a | 2010 | 1 | n/a | $25,000 | $25,000 | 1. Conduct assessment to identify densities of bivalves on beaches. | No |
| HK-14 | Population and distribution of Crabs | Cowichan Bay | Cowichan Bay, Samsun Narrows, Satellite | Crabs | n/a | 2010 | 1 | n/a | $50,000 | $50,000 | 1. Conduct population assessment of crabs within the Bay. | No |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Channel |  |  |  |  |  |  |  |  |  |
| HK-15 | Water Quality Monitoring | Cowichan Bay | Cowichan Bay | All | n/a | 2006 | 10 | Seasonal | $20,000 | $200,000 | 1. Conduct water quality monitoring. 2. Tissue analysis of crabs 3. Annual reporting of results ($5,000). | No |
|  |  |  |  |  |  |  |  | Totals | $775,000 | $1,265,000 |  |  |

Habitat Gain Recovery Actions

Appendix D4.    Table of recovery actions to directly affect habitat gain with preliminary project designs and cost estimates. (donated labour and materials are costed for the purposes of this recovery plan).

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HG-1 | Assess / Improve Cowichan Lake Fishway | Cowichan Lake | Lake outlet | Coho, Trout | Fry | 2008 | 1 | n/a | $70,000 | $70,000 | 1. Assess upstream fish passage for juvenile salmon and trout 2. Design/construct an improved fish passage facility to effectively pass juvenile salmon and trout | No |
| HG-2 | Stabilize Sediment Sources | Cowichan Lake Tributaries | Robertson, Nixon | Steelhead, Coho | Adult, Fry, Parr | 2009 | 5 | Annual | $50,000 | $250,000 | 1. Conduct investigations to identify / measure / map major sediment sources in each watershed. 2. Assess and cost a range of geotechnical and engineering options designed to significantly reduce sediment loading from priority point sources, and to develop a sediment management and fish passage strategy for the alluvial fans. This phase will produce detailed engineering surveys / designs for the major sediment sources, and potentially bypass channels for fish passage in the alluvial fan zone. 3. Implement remedial measures at priority sediment-sources. It is expected the implementation phase of this project will take 2-3 years depending on available budgets and the scope of work to be done. Coincident with physical remediation works, a monitoring program will be initiated to determine the effectiveness of prescribed treatments. | No |
| HG-3 | Improve Summer Baseflows (rearing) | Cowichan Lake Tributaries | Halfway Ck | Coho | Fry | 2012 | 2 | Annual | $75,000 | $150,000 | 1. Storage from Fairservice (Cook's) Lake could yield a flow release of 2.3 L/s for approximately 150 days. Fairservice Lake is a 2.1 ha marsh and would require 2 m of storage. 2. Further hydrological analysis needed to determine if 2.3 L/s will be adequate flow to maintain habitat. | No |
| HG-4 | Improve Off-channel Rearing | Cowichan Lake Tributaries | Shaw (Wren), Nixon, Sutton | Steelhead, Coho | Adult, Fry, Parr | 2010 | 3 | Annual | $100,000 | $300,000 | 1. Conduct topographical survey and evaluate feasibility for potential off-channel construction. 2. If feasible, complete off-channel design and construct. 3. Three streams identified for off-channel development – for each stream cost estimate assumes: $15,000 for survey and design; $85,000 for construction. | No 2007 Sutton Creek sediment removal in lower section as part of PEP program |
| HG-5 | Channel / Slope Stabilization | Cowichan River Mainstem | Stoltz Slide, Block 51 and other significant sediment sources | Chinook | Fry, Adult, Parr | 2008 | 4 | Annual | $300,000 | $1,200,000 | 1. Once a course of action has been endorsed from Project HK3, remedial work will begin at priority sediment sources. Potential work at Stoltz Slide includes: a) in the mainstem: channel excavation, terraced toe berm and partial weir; and b) on the slide: gully stabilization using bioengineering treatments. It is expected the implementation phase of this project will take 2-3 years | YES, ongoing work at Stoltz with silde and upslope stabilization projected for 2008. |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  | depending on available budgets and the scope of work to be done. Coincident with physical remediation works, the monitoring program will be initiated to determine the effectiveness of prescribed treatments. |  |
| HG-6 | Improve Instream Habitat (rearing, access) | Cowichan River Tributaries | Somenos, Holt are priorities | Steelhead, Coho | Adult, Fry, Parr | 2006 | 3 | Annual | $50,000 | $90,000 | 1. Conduct fish passage assessment, identify opportunities to improve rearing habitat and prepare rehabilitation designs. 2. Implement remedial measures at culverts and construct instream / off-channel rehabilitation works. | No |
| HG-7 | Secure Riparian Corridor | Cowichan River Mainstem | Upper River between Block 51 and Lake outlet | Chinook, Steelhead, Coho, Chum | Fry, Adult, Parr | 2007 | 19 | Annual | $50,000 | $900,000 | 1. Most of existing riparian corridor from Cowichan River mouth to Block 51 is owned by the Crown, which offers long-term protection of the riparian vegetation. The section of river upstream of Block 51 is the primary spawning area for Chinook and steelhead but has only a few land parcels under Crown ownership. 2. In cooperation with private land owners, opportunistically purchase or secure through conservation agreements land parcels along both sides of the river to provide protection for the riparian corridor and channel over the long term. 3. Additional funds will need to be leveraged (The Land Conservancy?) | No Some protection afforded by RAR setbacks |
| HG-8 | Improve Off-channel Rearing | Cowichan River Mainstem | Major Jimmy’s, Bible Camp, Lamb’s, Trestle, Channel 83A (total area affected = 20,000 m2) | Chinook, Chum, Coho, Steelhead | Fry, Parr | 2006 | 5 | Annual | $100,000 | $500,000 | 1. Implement remedial measures to constructed side channels at Lamb’s and Trestle that include upgrading the intake structures and adding LWD cover. 2. Improve instream cover in Major Jimmy’s channel by adding LWD to 14 specified sites. 3. Enhance an existing overflow channel at Bible Camp by re-constructing the channel, placing LWD in pool habitats, and providing a river intake that could be regulated. 4. Install intake structure and improve natural overflow inlet in Channel 83A | No Hatchery Channel upgrades and complexing undertaken in 2007 in partnership between MOT and Cowichan Tribes. |
| HG-9 | Raise Cowichan Lake Weir to Increase Summer River Flows | Cowichan River Mainstem | Cowichan Lake Weir | Chinook, Steelhead, Chum, Coho | Fry, Adult, Parr | 2006 | 1 | n/a | $250,000 | $250,000 | 1. Raise the Weir to increase summer flows in mainstem, to improve fish migration, and to improve connectivity of river to off-channel habitats. 2. Decision on feasibility and new height of Weir dependent on recommendations from Cowichan Water Management Plan. | Water Management Plan funded in 2005 by CVRD completed in 2007, CVRD decision to remove recommendation on raising weir from report |
| HG-10 | Improve Fish Passage | Cowichan River Mainstem | Skutz Falls Fishway | Chinook | Adult | 2006 | 2 | Annual | $50,000 | $100,000 | Assess current Chinook passage capability through Skutz Falls fishway under low flow conditions 2. Implement remedial measures to improve Chinook passage at fishway | No |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HG-11 | Improve Summer Flows (rearing) | Cowichan River Tributaries | Richards, Holt, Averill | Coho, Steelhead | Fry | 2008 | 3 | Annual | $50,000 | $150,000 | 1. Conduct assessment of water storage potential to improve summer baseflows and rearing. 2. Prepare water storage designs and flow management plans for suitable sites. | No |
| HG-12 | Improve Riparian Corridor | Cowichan River Tributaries | Somenos, Quamichan, Richards, Averill, Bings | Coho, Steelhead | Fry, Adult, Parr | 2010 | 10 | n/a | $50,000 | $500,000 | 1. In cooperation with private land owners, opportunistically rehabilitate riparian zones and establish riparian management plans for crossings, pastures, etc. 2. Initiate demonstration riparian projects with landowners, particularly on agricultural lands. | No |
| HG-13 | Improve Fish Migration | Koksilah River Mainstem | Marble Falls Fishway | Chinook, Steelhead, Chum, Coho | Adult | 2008 | 2 | Annual | $50,000 | $100,000 | 1. Assess current Chinook passage capability through Marble Falls fishway. 2. Implement remedial measures to improve fish passage. | No |
| HG-14 | Improve Riparian Corridor | Koksilah River & Tributaries | Mainstem, Norrie, Kelvin | Chinook, Steelhead, Chum, Coho | Fry, Adult, Parr | 2010 | 10 | n/a | $50,000 | $500,000 | 1. In cooperation with private land owners, opportunistically rehabilitate riparian zones and establish riparian management plans for crossings, pastures, etc. 2. Initiate demonstration riparian projects with landowners, particularly on agricultural lands. | No |
| HG-15 | Stabilize Sediment Sources | Koksilah River & Tributaries | Mainstem, Glenora, Norrie, Kelvin | Chinook, Steelhead, Chum, Coho | Fry, Adult, Parr | 2012 | 5 | Annual | $50,000 | $250,000 | 1. Conduct investigations to identify / measure / map major sediment sources in each watershed. 2. Assess and cost a range of geotechnical and engineering options designed to significantly reduce sediment loading from priority point sources. This phase will produce detailed engineering surveys / designs for the major sediment sources. 3. Implement remedial measures at priority sediment-sources. It is expected the implementation phase of this project will take 2-3 years depending on available budgets and the scope of work to be done. Coincident with physical remediation works, a monitoring program will be initiated to determine the effectiveness of prescribed treatments. | No |
| HG-16 | Improve Off-channel Rearing | Koksilah River & Tributaries | Mainstem, Glenora | Chinook, Steelhead, Chum, Coho | Fry, Parr | 2012 | 3 | Annual | $100,000 | $300,000 | 1. Based on rehabilitation opportunities from Project HK-8 prepare off-channel designs for suitable sites. 2. Construct off-channel habitats, intake structures, LWD structures, etc. at suitable sites. | No |
| HG-16a | Assess culvert/fish passage | Koksilah River and Tributaries | Glenora and Industrial Area | Chinook, Steelhead, Chum and Coho | Fry, Adult, Parr | 2008 | 1 |  |  |  | Assess current drainage patterns and storm water greenways linked to side channel habitat. Develop hybrid RAR setbacks and potential drainage features Develop multi stakeholder partnerships with residents, agricultural interests, industrial areas as well as agencies including DFO, MOE, MOT and CVRD | No |
| HG-17 | Recapture Off-channel Rearing | Cowichan Estuary | Cowichan Estuary | Chinook, Steelhead, Chum, Coho | Fry | 2008 | 5 | Annual | $100,000 | $500,000 | 1. Based on recommendations from Project HK-10, implement rehabilitation measures to recapture off-channel sloughs and backwaters, and perennial flood channels. | No |

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HG-18 | Eelgrass Expansion | Cowichan Estuary | Cowichan Estuary | Salmon, Shellfish | Fry | 2006 | 10 | Annual | $50,000 | $500,000 | Based on recommendations from Project HK-11, implement protection / rehabilitation measures to increase and improve the condition of tidal vegetation, particularly eelgrass. follow up with Paul R comments regarding the potential use of mesh enclosures ( eg goey duck farming) as artificial supports to eel grass colonization. | No 2006/7 CCLT with Seachange Conservation funded and undertook a Eel grass restoration pilot project in selected sites in Cowichan Bay. |
| HG-19 | Clam Beach Seeding | Cowichan Bay | Cowichan Bay | Clams | n/a | 2011 | 2 | Annual | $20,000 | $40,000 | 1. Assess effectiveness of seeding through population growth and production monitoring (considered as an experiment). | No |
| HG-20 | Maintenance | All | All | All | All | 2006 | 20 | Semi | $100,000 | $1,000,000 | 1. Monitor and maintain restoration works | No |
|  | and Monitoring |  |  |  |  |  |  | annual |  |  | 2. Report on effectiveness |  |
|  |  |  |  |  |  |  |  | Totals | $1,715,000 | $7,650,000 |  |  |

Stewardship and Education Recovery Actions

Appendix D5. Table of recovery actions to directly affect stewardship and education activities with preliminary project designs and cost estimates. (donated labour and materials are costed for the purposes of this recovery plan).

| Project Code | Objective | Zone | Location | Species (10 & 20) | Life Stage (10 & 20) | Start Year | No. of Years | Frequency | Annual Cost | Total Cost | Project Description | Currently Funded |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SW-1 | Riparian Management | Cowichan Lake & Tributaries | Lake shore, Robertson, Shaw, Nixon, Sutton, Meade, Cottonwood | Chinook, Steelhead, Chum, Coho | Adult, Fry, Parr | 2006 | 15 | Annual | $15,000 | $225,000 | 1. Develop public information materials on best management practices and practical land and riparian management strategies that protect / rehabilitate streamside corridors. 2. Develop materials on methods and practices that reduce non-point source pollution impacts. 3. Target landowners managing agricultural lands and forest harvesting companies. | No Potentially funded by the CVRD as a outreach program |
| SW-2 | Riparian Management | Cowichan River & Tributaries | Mainstem, Somenos | Chinook, Steelhead, Chum, Coho | Adult, Fry, Parr | 2006 | 15 | Annual | $15,000 | $225,000 | Develop public information materials on best management practices and practical land and riparian management strategies that protect / rehabilitate streamside corridors. 2. Develop materials on methods and practices that reduce non-point source pollution impacts. 3. Target landowners managing agricultural lands and forest harvesting companies. 4. work with the Somenos Management Committee and North Cowichan to more effectively distribute information. | No Potentially funded by the CVRD as a outreach program |
| SW-3 | Water Conservation | Cowichan River & Tributaries | Mainstem, Somenos | Chinook, Steelhead, Chum, Coho | Adult, Fry, Parr | 2006 | 15 | Annual | $15,000 | $225,000 | 1. Develop public information materials on best management practices for water conservation through more efficient use of water. 2. Target landowners with water withdrawal licenses. | No Potentially funded as an outcome of the Cowichan Water Basin Study |
| SW-4 | Riparian Management | Koksilah River & Tributaries | Mainstem, Norrie, Glenora, Kelvin | Chinook, Steelhead, Chum, Coho | Fry, Adult, Parr | 2006 | 15 | Annual | $15,000 | $225,000 | 1. Develop public information materials on best management practices and practical land and riparian management strategies that protect / rehabilitate streamside corridors. 2. Develop materials on methods and practices that reduce non-point source pollution impacts. 3. Target landowners managing agricultural lands and forest harvesting companies. | No Potentially funded by the CVRD as a outreach program |
| SW-5 | Water Conservation | Koksilah River & Tributaries | Mainstem, Norrie, Glenora, Kelvin | Chinook, Steelhead, Chum, Coho | Fry, Adult, Parr | 2010 | 15 | Annual | $15,000 | $225,000 | 1. Develop public information materials on best management practices for water conservation through more efficient use of water. 2. Target landowners with water withdrawal licenses. | No Potentially funded as an outcome of the Cowichan Water Basin Study |
| SW-6 | Protect Intertidal Habitat | Cowichan Estuary | Cowichan Estuary | Shellfish and Vegetation | n/a | 2005 | 20 | As needed | $5,000 | $100,000 | 1. Manage foreshore developments to protect and recover intertidal habitats by adhering to community development plans and establishing protocols for the review of development proposals. | No |
| SW-7 | Protect Intertidal Habitat | Cowichan Bay | Cowichan Bay | Shellfish and Vegetation | n/a | 2005 | 20 | As needed | $5,000 | $100,000 | 1. Manage foreshore developments to protect and recover intertidal habitats by adhering to community development plans and establishing protocols for the review of development proposals. | No |
| SW-7a | Protect intertidal Habiata | Cowichan Bay and Estuary | Cowichan Bay | All | all | 2007/8 | ongoing |  |  |  | Support the review and revitalization of the Cowichan Estuary Environmental Management Plan (CEEMP) | MOE contract with Roger Hunter |
| SW-8 | Reach out to communities and Schools | All | All | All fish and Shellfish | all | 2006 | 15 | Annual | $15,000 | $225,000 | 1. Develop educational material on the freshwater and marine ecosystems of the Cowichan-Koksilah basins, including existing flora and fauna, current habitat conditions and threats, and activities that can be undertaken to prevent impacts to environment. 2. Target general community and K-12 school shildren |  |